| Product Name: | ACC9100 UHF Long Range Integrated Reader/Antenna |  |  |
| --- | --- | --- | --- |
| Product Details: |  |  |  |
| Support protocol |  | ISO18000-6B/ISO18000-6C(EPC G2) |  |
| Working frequency |  | ISM 902MHz～928MHz,Or 920MHz～925MHz |  |
| Custom |  | 860MHz～960MHz |  |
| Working mode |  | FHSS or working mode of fixed frequency pulse transmitting set by software |  |
| Transmit power |  | 20dBm～30 dBm(set by software) |  |
| Read-Write performance |  |  |  |
| Read speed |  | The average read time for single card is less than 10ms per 64 bits |  |
| Read distance |  | 8m～15m(according of tag and entironment) |  |
| Write speed |  | 8bits less than 30ms |  |
| Write distance |  | 4m～7m(according tag) |  |
| Read prompt |  | Buzzer |  |
| Data Port interface |  |  |  |
| RS232 Port |  | Yes |  |
| RS485 Port |  | Yes |  |
| Weigand Port |  | Weigand26/34 |  |
| Trigger port |  | Yes |  |
| TCP/IP Port |  | Custom |  |
| Electrical: |  |  |  |
| Power supply |  | DC+9V,4A |  |
| Power consumption |  | 6W |  |
| Size and weight |  |  |  |
| Dimension |  | 450mm×450mm×60mm |  |
| Weight |  | 3700g |  |
| Working environment |  |  |
| Working temperature | -30℃～70℃ |  |
| : ACC Systems Inc. 1 Robert Lane, Glen Head, NY 11545 ph. 516-674-0191 Email: rfid@accsystemsinc.com web: www.accsystemsinc.com |  |  |