ACC Micro RFID Handheld Reader Specifications

CPU ARM7 or ARM9

Memory 512KB RAM / 2MB FLASH or 64MB RAM / 8MB FLASH

Proof of Data Non volatile memory

Date/Time Realtime clock

Interface USB (serial) or USB Mass Storage, USB HiD, USB Ethernet

Barcode 1D Laser Class1 (EAN/UPC 8n EAN/UPC13, Code 39, Code128, EAN128, Interleaverd 2of5, CODABLOCK, HIBC,

# Pharmacode)

# or

2D CMOS Camera module all 1D plus Code49, EAN/UCC Composite, PDF417, Micro PDF, MaxiCode, DataMatrix, Aztec,

Aztec Mesa, QR Code, OCR)

RFID 125KHz (Unique, Q5, Hitag1, Hitag2, Hitag S)

13,56MHz (Mifare 1K, 4K, UL)

13,56MHz (I-Code SLI, TagIt HF1, MyD)

UHF Class1 Gen2

Wireless Bluetooth (MTSU.WML-C40_NH) Class 1

Audio Speaker WAV-Files MP3

LED red/green/yellow/blue

Keys 2 (free programmable) 1 ON/OFF

Dimensions 116 x 50 x 31mm

Weight 80 g

Rechargeable Battery 1050 mAh Li-Ion

Battery Charging Over USB interface Power supply

Batteries Standard  3 - AAA Batteries

RTC Battery supply during changing main battery

insures time setup not lost

Housing Double wall Inside: Shock resistant ABS

Outside: Stressable rubber

Temp. range -10°C bis +50°C

Protection Class IP 54

Drop 6 ft on concrete

smartSCANNDY 2 smartSCANNDY 1